## Slide 1: An Ultra Low Power DLL Design
Yanqing Zhang
yanqing@virginia.edu

## Slide 2: Outline
Motivation
Problem Statement
Expected Outcomes
Approach
  Architectural Considerations
  Block Design
Results
  Functionality
  Power/frequency scalability
  Jitter analysis
Discussion
Conclusion
Notes: Crystals can’t provide a full reference
Literature shows this is the way to go…maintains advantages of DLL

## Slide 3: Motivation and Application Space
Why do we need a DLL for ultra low power apps?
  Pulse generation for latched based timing/time borrowing
  Generation of different phase clocks for SoC applications
DLLs fit application needs
  Less jitter (no VCO)
  Ensured stability
  Closed loop
Notes: Crystals can’t provide a full reference
Literature shows this is the way to go…maintains advantages of DLL

## Slide 4: Outline
Motivation
Problem Statement
Expected Outcomes
Approach
  Architectural Considerations
  Block Design
Results
  Functionality
  Power/frequency scalability
  Jitter analysis
Discussion
Conclusion
Notes: Crystals can’t provide a full reference
Literature shows this is the way to go…maintains advantages of DLL

## Slide 5: Problem Statement
…but clock generation could RUIN purpose of low power
Therefore, need a low power, reliable(to the extent of the frequency) design

## Slide 6: Problem Statement
Will try to compare with lowest power reported in sampled literature [8]
Design specifications:
  Main frequency 100 MHz
  P2p jitter <5% of clock period
  Power <50 uW
  False lock prevention

## Slide 7: Outline
Motivation
Problem Statement
Expected Outcomes
Approach
  Architectural Considerations
  Block Design
Results
  Functionality
  Power/frequency scalability
  Jitter analysis
Discussion
Conclusion
Notes: Crystals can’t provide a full reference
Literature shows this is the way to go…maintains advantages of DLL

## Slide 8: Expected Outcomes
Meets specifications
Evaluations:
  Power consumption across VDD, f
  Acquisition range across VDD
  Jitter analysis across f
  Supply noise sensitivity
  Process variation robustness
  Digital integration

## Slide 9: Outline
Motivation
Problem Statement
Expected Outcomes
Approach
  Architectural Considerations
  Block Design
Results
  Functionality
  Power/frequency scalability
  Jitter analysis
Discussion
Conclusion
Notes: Crystals can’t provide a full reference
Literature shows this is the way to go…maintains advantages of DLL

## Slide 10: Approach: Architecture Considerations
Literature search
  What options are available to scale power down?
ADDLLs
First observation:
  1. Scale down VDD, huge amounts of power saved (VDD = 0.5V)
[4]
[6]

## Slide 11: Approach: Architecture Considerations
2. How do we make the DLL fully digital?
CP
PD
LPF
VCDL
Vcont
Bang-bang PD
Inverter based
Digital signal
Counter

## Slide 12: Approach: Architecture Considerations
3. VCDL considerations
  String of inverters consume excess power
  Only need enough inverters to achieve desired phase resolution
  Constrain current through header/footers (only need enough for required delay)
Digital up/down Counter
Bang-bang PD
VCDL
Control_Word<5:0>
…
1 2 4 8 …
…
1 2 4 8 …

## Slide 13: Approach: Architecture Considerations
4. False lock prevention
  Add a reset to counter, counter starts at 6’b000000
  Delay starts at smallest, so slowly increases to desired value
Notes: Smaller the frequency, the longer the lock acquisition time

## Slide 14: Approach: Block Design
Bang-bang PD
  Static CMOS
  Limit setup/hold time for resolution

## Slide 15: Approach: Block Design
Control counter
  Synthesized
  Problem with freepdk cell characterization

## Slide 16: Approach: Block Design
VCDL
  Weak latches to help with variation
  Inverters sized to sink maximum current supplied by header(W/L=420n/45n)
  Header lengths sized up to decrease leakage, total current=maximum current sunk by inverter(W/L=90n/800n)

## Slide 17: Outline
Motivation
Problem Statement
Expected Outcomes
Approach
  Architectural Considerations
  Block Design
Results
  Functionality
  Power/frequency scalability
  Jitter analysis
Discussion
Conclusion
Notes: Crystals can’t provide a full reference
Literature shows this is the way to go…maintains advantages of DLL

## Slide 18: Results: Functionality
Functional simulation @0.5V, locking to 100 MHz
15 uW, 230 ps dithing jitter
30 clock cycle acquisition, control_word=6’b011110;

## Slide 19: Results: Functionality
Supply Voltage | Maximum Frequency | Minimum Frequency
0.5V | 166 MHz | 10 MHz
0.4V | 40 MHz | 3 MHz
0.3V | 6.6 MHz | 500 kHz
Acquisition range across VDD :
Sufficient across ultra low power applications:
  0.5 V = above threshold
  0.4 V = at threshold
  0.3 V = sub-threshold
  Vthp = -0.38 V, Vthn = 0.41 V

## Slide 20: Results: Frequency/Power Scalability

## Slide 21: Results: Frequency/Power Scalability

## Slide 22: Results: Jitter Analysis
Dithering jitter, caused by resolution of bang-bang PD (230ps @ 100 MHz)
For same frequency, decreases with VDD decreasing
  Seems to suggest, that for a locking frequency, should try to use lowest VDD available

## Slide 23: Results: Jitter Analysis
For same supply and different locking frequency, jitter increases as frequency decreases
  The more reason to scale VDD appropriately

## Slide 24: Results: Jitter Analysis
Supply sensitivity, typically high for digital circuits
  Worsens as VDD decreases
Fails to lock because of duty cycle distortion
  Bad sizing
  Needs duty cycle correction
Voltage regulator needed
  0.67% VDD supply noise exemplified
Operating Point | Dithering Jitter Only | Supply Noise | Jitter w/ Supply Noise
100MHz @0.5V | 230 ps | 10% VDD, 10% f | 3.97 ns
10MHz @0.4V | 13 ns | 10% VDD, 10% f | Fails to lock
3 MHz @0.3V | 15 ns | 10% VDD, 10% f | 446 ns
10MHz @0.4V | 13 ns | 2.5% VDD, 10% f | 27.3 ns

## Slide 25: Results: Jitter Analysis
Supply sensitivity, typically high for digital circuits
  Worsens as VDD decreases
Fails to lock because of duty cycle distortion
  Bad sizing
  Needs duty cycle correction
Voltage regulator needed
  0.67% VDD supply noise exemplified
Operating Point | Dithering Jitter Only | Supply Noise | Jitter w/ Supply Noise
100MHz @0.5V | 230 ps | 0.67% VDD, 10% f | 373 ps
10MHz @0.4V | 13 ns | 0.67% VDD, 10% f | 20.7 ns
3 MHz @0.3V | 15 ns | 0.67% VDD, 10% f | 41 ns

## Slide 26: Results: Jitter Analysis
Process variations
μ= 3.577 ns
σDLL = 365 ps, σinv = 214 ps
DLL has less outliers

## Slide 27: Outline
Motivation
Problem Statement
Expected Outcomes
Approach
  Architectural Considerations
  Block Design
Results
  Functionality
  Power/frequency scalability
  Jitter analysis
Discussion
Conclusion
Notes: Crystals can’t provide a full reference
Literature shows this is the way to go…maintains advantages of DLL

## Slide 28: Discussions
Needs duty cycle correction
Temperature analysis not done
Reference feedthrough analysis, reference assumptions
Digital control resolution tradeoffs: header array sizing, number of inverters
Need industry supplied MC models
MC analysis @ different supply voltages
Regulator robustness/power vs. supply induced jitter analysis

## Slide 29: Conclusions
Meets design specifications (minus process variation effects somewhat)
Advantages:
  Digital integration
  Ultra low power
  Acceptable jitter
Disadvantages:
  Lock acquisition time lengthens with slower frequency o(N2)
  No duty cycle correction
  Supply noise sensitivity

## Slide 30: Conclusions
Beats [8]….for now (not considering process variations…)
 | P2p jitter | Frequency | Power | % Jitter/Freq | xPower | Main Contribution
[8] | 30 ps | 100 MHz | 0.3 mW | 0.3% | . 9 uW | Fast lock acquisition
YQ | 373 ps | 100 MHz | 15 uW | 3.73% | 0.5595 uW | Low Power